## Slide 1: Rckemac in Detail
Jae min choi
SNUCSE

## Slide 2: Flow
emac_module_init
emac_module_exit
emac_open
emac_stop
emac_rx
emac_tx

## Slide 3: Registers in Use
Global Register Bank (GRB) : register located inside FPGA

## Slide 4: Registers in Use
Configuration Register Bank (CRB) : set of configuration registers for SCC cores
  Control enabling local reset, core initialization & configuration, core interrupt handling, and L2 cache configuration
  Each SCC core, L2 cache controller, and global clocking unit (GCU) has a dedicated config register
  Writable by any core or the system interface unit
  Byte-wise access not supported
  Should perform read-modify-write on all 32 bits of a config register

## Slide 5: Helper functions & macros
static int emac_readl (void *addr)
  Read long from eMAC at addr
  Implemented with 2 readl calls
static void emac_writel (int value, void *addr)
  Write long value to eMAC at addr
  Implemented with writel
RA(_x, _y)
  GRB address + (_x)+ (_y * 4)
RA_CRB(_x)
  CRB address + (_x)
All accesses to the registers are done via these macros
Both polling and interrupts can be implemented
  Will suppose using interrupt

## Slide 6: emac_module_init
Map GRB to 0xF9000000 with size 0x10000
Map CRB to 0xF8000000 with size 2 * (page size)
Read tile ID from (CRB + 0x0100) and determine core position
  Bits 06:03 – x
  Bits 10:07 – y
  Bits 02:00 – z
Set core number
Get FPGA/sccKit port settings from (GRB + 0x822C)
Create eMAC interface (emac0, …)
  Initilize Xilinx IP port (init_xilinx_port)
  Allocate netdev structure (alloc_netdev and emac_init)
  Allocate priv structure (netdev_priv and memset)

## Slide 7: init_xilinx_port
Called from emac_module_init to create an eMAC interface
Get transmitter & receiver address from GRB
Disable TX/RX flow control of eMAC (GRB + 0x32C0)
  Set top 3 bits of flow control configuration to zero
Enable transmitter & set to full duplex mode (GRB + 0x3280)
  Half duplex (Bit 26) = 0
  Transmit enable (Bit 28) = 1
  Reset (Bit 31) = 0
Enable receiver & set to full duplex mode (GRB + 0x3240)
  Length/type error check disable (Bit 25) = 1
  Half duplex (Bit 26) = 0
  Receiver enable (Bit 28) = 1
  Reset (Bit 31) = 0

## Slide 8: init_xilinx_port
Set speed of eMAC to 1Gb/s (GRB + 0x3300)
  Bit 31 = 1, Bit 30 = 0
Set to promiscuous mode (GRB + 0x3390)
  Bit 31 = 1
Be sure to conduct sanity checks after changing register values

## Slide 9: emac_init
Called by alloc_netdev
Setup net_device structure
  ether_setup to setup standard infos
  Assign driver specific functions (open, stop, ioctl, stats, …)

## Slide 10: emac_open
Called when eMAC interface is opened
Read tile ID and determine core position
Set interrupt request (IRQ) address
  Core 0: CRB + 0x10
  Core 1 : CRB + 0x18
Get offset, subdest, route, mode
  First read value from (CRB + 0x800, Core 0) or (CRB + 0x1000, Core 1)
  Calculate offset, etc. by shifting this value
Setup Ethernet port (setup_emac)
Set network address
  First get MAC address (get_mac_address)
  And iterate for loop to consecutively save lower 8 bits of address in dev->dev_addr
Enable interrupt
  Clear interrupt (emac_clear_interrupt)
  Read value from (GRB + 0xD200 + priv->pid * 2 * 4) and change it
  Change value in (GRB + 0xD800+ priv->pid * 4)
  Call request_irq and check its return value
Start network queue (netif_start_queue)

## Slide 11: setup_emac
Called from emac_open
Reception configuration
  Set up ring buffer space
    Set priv->rx_buffer_max
    Allocate priv->rx_buffer using alloc_buffer
  Set start address of RX buffer (GRB + 0x9000)
  Read RX buffer write offset (GRB + 0x9200)
  Set RX buffer write offset to RX buffer read offset (GRB + 0x9100)
  Set RX buffer size (GRB + 0x9300)
  Set RX buffer threshold (GRB + 0x9400)
  Set RX mode (GRB + 0x9500)
  Save MAC address (HI: GRB + 0x9600, LO: GRB + 0x9700)
  Activate network port (GRB + 0x9800)
Transmission configuration

## Slide 12: TODO
emac_rx
emac_tx
emac_stop
emac_module_exit